Birch Biolime® 90

High Calcium Quicklime - Calcium oxide CaO

Biolime is a coarse, white calcium oxide powder which is made by crushing and screening quicklime.  Biolime is Specifically developed for sludge treatment.

Typical		Specification

Chemical Analysis     					% Mass		% Mass

(Dry Basis)	lankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlankBlank	Calcium oxide			CaO			94			90.0 min*

Silica				SiO2			1.9

Magnesium oxide		MgO			0.42

Aluminium oxide		Al2O3			0.23

Ferric oxide			Fe2O3			0.13

Carbon			CO2			2.6			6.0 max*

Sulphur			SO3			0.03

Physical Analysis

Reactivity			Time (Mins)		Temp. C		Temp. Range C

0			20

5			71			50 min.

Particle Size			Microns		Passing %		Passing Range %

180			100

90			98			90-100

45			83

Mean Particle Size		Microns		2-3

Bulk Densities			kg/m3			900

* Specification Based on in Process testing of Burnt Lime 40 Feedstock.

All product specifications are based on tests carried out prior to despatch of product.

An application has been made for authorisation of this material to be used as a biocidal product under Regulation (EU) No 414/2013, as amended

This specification relates to product numbers: 	117501 - BULK		Last Revision Date: April 2018

Storage Recommended minimum bulk silo capacity for quicklime/Aqualime® 60m3, Ultralime® 120m3.

Further advice/information available on request.

Safety 	Refer to our Safety Data Sheet.